## Slide 1: PPP Survey PPP Execution Example
Data Communication assignment #1-4 #1-5

## Slide 2: Setting Virtual Machine
Set up serial port in virtual machine
  Need 2 VMs for communicate

## Slide 3: Serial Port Set Up in VM1
- 포트/파일 경로: \\.\pipe\com1으로 설정(1: 포트번호)
ex) 포트번호를 COM1로 설정, 포트/파일 경로 \\.\pipe\com1 로 설정
- vm1은 존재하는 파이프/소켓에 연결 체크 안함, vm2는 체크
- virtual machine 실행 시 존재하는 파이프/소켓에 연결을 체크하지 않은 vm부터 실행시켜야함
(즉 이 예제에선 vm1부터 실행시켜야 vm이 모두 켜짐)

## Slide 4: Serial Port Set Up in VM2

## Slide 5: What is a Null Modem.
Null modem is a communication method to connect two DTEs
(computer, terminal, printer etc.) directly
using an RS-232 serial cable.

## Slide 6: Null modem in virtual machine

## Slide 7: PPP Connection
Check PPP applications
$ which pppd
$ which pppdump
Install : # apt-get install ppp

## Slide 8: pppd connection
Command format
  Local IP : My IP address
  Remote IP : Correspond IP address
  ttyname : /dev/ttySx (x : port number)
  record <path> : full path (ex : /root/test01)
  Speed : 38400 (bps)
# pppd -detach crtscts lock debug record <path> noccp <local IP>:<remote IP> ttyname speed

## Slide 9: ttySx mapping
# setserial –g /dev/ttyS*

## Slide 10: pppd command option
Command option
- option ($man pppd)
· crtscts: specifies that pppd should set the serial port to use h/w flow control.
· lock: specifies that pppd should create a UUCP-style lock file for the serial device
to ensure exclusive access to the device. By default, pppd will not create a lock
· debug: Enables connection debugging facilities. If this option is given, pppd will log the
contents of all control packets sent or received in a readable form.
· record <path>: Specifies that pppd should record all characters sent and received to
path
· <local IP>:<remote IP>: Set the local and/or remote interface Ip address.
· ttyname: Use the serial port called ttyname to communicate with the peer.
· speed: An option that is a decimal number is taken as the desired baud rate for the
serial device.
# pppd -detach crtscts lock debug record <path> noccp <local IP>:<remote IP> ttyname speed

## Slide 11: pppd connection command
pppd execution
  Terminal1 (VM1)
  Terminal2 (VM2)
    Same as terminal1, only swap local IP for remote IP
  record /root/test01 : Set the path for dump file
# pppd -detach crtscts lock debug record /root/test02 noccp 10.1.3.20:10.1.3.10 /dev/ttyS0 38400
# pppd -detach crtscts lock debug record /root/test02 noccp 10.1.3.10:10.1.3.20 /dev/ttyS0 38400

## Slide 12: pppd connection example - debug

## Slide 13: PPP frame analysis
Dump file output
#pppdump –h <path>
  The pppdump utility converts the files written using the record option of pppd into a human-readable format.
  path : /root/test01 or /root/test02

## Slide 14
result of pppdump

## Slide 15: HDLC PPP LCP frame example

## Slide 16: Frame Delimiter
Frame delimiter (flag)
  A frame delimiter marks the end of one frame and the beginning of another. A frame delimiter at the end of a frame may also mark the start of the next frame.
  The next frame is after an idle period
  In case of continuous communication

## Slide 17: Homework #1-4 (5)
pppd execution
  Execute pppd following this command line
submission
  Result screenshot
    pppd connection debug output (like page 12)
  Report
    Explain PPP frame exchange order with reference to RFC documents.
pppd -detach crtscts lock debug noccp record /root/test01 <local IP>:<remote IP> /dev/ttyS0 38400

## Slide 18: Homework #1-4 (5)
pppd 명령어를 사용하여 ppp configuration 과정을 pppd connection debug 화면을 기반으로 설명

## Slide 19: Homework #1-5 (10)
  Result screenshot
    pppdump output (like page 14)
  Report
    Analyze pppdump output to fit a frame format of PPP.
      LCP frames, IPCP frames and Data frame (IPv4).
  Open pppdump packet

## Slide 20: Homework #1-5 (10)
1. ppp 실행 후, pppdump 패킷 분석 (LCP, IPCP, IP Frame이 왜 해당 값을 갖는지)
모든 과제에는 반드시 결과 캡쳐화면을 첨부해주셔야합니다.

## Slide 21: References
http://www.tldp.org/HOWTO/PPP-HOWTO/
http://linux.about.com/library/cmd/blcmdl8_pppdump.htm
RFC 1661, RFC 1662, RFC 1332
James Carlson, “PPP Design, Implementation, and Debugging 2nd edition,” Addison-Wesley, July 2000.